## Slide 1
EcoDrive
AI-Powered Vehicle Emissions Estimation
and Eco-Driving Recommendation System
B.Tech Final Year Project Report
Department of Computer Science & Engineering
Uttarakhand Technical University, Dehradun
Academic Year 2025–2026

## Slide 2
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
CONTENTS
01
Introduction
Background, Motivation & Objectives
02
System Analysis
Existing Systems & Gap Analysis
03
System Design
Architecture, Model & Tech Stack
04
Implementation
Physics Engine, ML & Dual-LLM
05
Results & Validation
Emission Estimates & Sensitivity
06
Conclusion
Limitations, Future Scope & References
2 / 21

## Slide 3
01
INTRODUCTION
Background, Motivation, Problem Statement & Objectives

## Slide 4
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Background & Motivation
The Challenge:
India has 320M+ registered vehicles — world's 3rd largest automobile fleet. Road transport accounts for 12–15% of national CO₂ emissions.
Cities like Delhi, Bengaluru, Pune, and Dehradun consistently rank among the most polluted globally, with vehicular exhaust as the primary cause.
The Gap: Individual vehicle owners have no accessible tool to quantify real-time environmental cost of trips. Existing solutions use static averages or are locked in research platforms.
EcoDrive's Solution:
Embeds a rigorous vehicle dynamics physics engine directly within a mobile application, enabling:
Personalised, trip-level emission computation
On-device AI for offline eco-driving advice
Real-time GPS, weather, and traffic fusion
Monte Carlo uncertainty quantification
Target: Indian semi-urban and rural driving contexts where connectivity is limited.
320M+
Registered Vehicles (India)
12–15%
National CO₂ from Transport
4
Fuel Types Supported
100+
Indian Vehicles in Dataset
Source: CPCB Annual Report 2023; SIAM 2024
4 / 21

## Slide 5
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Problem Statement & Objectives
Five Critical Limitations
1. Static emission factors — uniform kg CO₂/km, ignoring speed, acceleration, terrain, AC load
2. No real-time telemetry — weather/traffic models require server-side computation
3. No uncertainty quantification — deterministic models give single point estimates
4. Poor multi-fuel support — most tools cover only petrol, neglecting CNG, Diesel, EV
5. No AI-driven personalisation — no LLM-based context-sensitive driving advice
Seven Project Objectives
1. Physics engine for 4 fuel types (Petrol, Diesel, CNG, EV)
2. Monte Carlo simulation (N=50) for 90% confidence intervals
3. Real-time GPS + weather + traffic telemetry fusion
4. Dual-LLM architecture (on-device MediaPipe + cloud fallback)
5. Multi-route CO₂ comparison via OSRM alternative routing
6. Room SQLite persistence with trip history & PDF reports
7. Android API 24+ support for maximum accessibility
Core Innovation: EcoDrive solves all five limitations within a single integrated Android application — the first consumer-facing tool to combine physics-grounded emission modelling, probabilistic uncertainty quantification, and on-device AI coaching for the Indian automotive context.
Chapter 1 — Introduction
5 / 21

## Slide 6
02
SYSTEM ANALYSIS
Survey of Existing Systems and Comparative Gap Analysis

## Slide 7
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Existing Systems & Comparative Analysis
Tool / System | Key Limitation | EcoDrive's Resolution
VAHAN Dashboard | Fleet aggregate only; no individual or trip-level estimation | Complete trip-level physics model; individual driver focus
Google Maps Eco Mode | Opaque model; no CO₂ output; no vehicle parameters; proprietary | Transparent physics equations; numerical CO₂ output; 90% CI
COPERT | Desktop only; no real-time data; inaccessible to consumers | Native Android; 5-API real-time fusion; consumer-friendly UI
OBD-II Apps | Hardware dongle required (INR 800–2,500); pre-2010 incompatible | Software-only; GPS + weather + physics; zero hardware cost
Generic Calculators | Single point estimate; no physics; no uncertainty; no AI | Monte Carlo CI; full physics; Dual-LLM AI coaching; open
Additional Differentiator: All existing tools lack India-specific factors. EcoDrive is calibrated to BS-VI standards, uses CPCB emission factors, and includes a dataset of 100+ Indian vehicles — making it the first emission estimation tool purpose-built for the Indian automotive context.
Chapter 2 — System Analysis
7 / 21

## Slide 8
03
SYSTEM DESIGN
Architecture, Computational Model, Data Flow & Technology Stack

## Slide 9
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
System Architecture & Data Flow
Six-Layer Architecture
Presentation
UI / Activities
Service Layer
GPS / Tracking
AI / ML Layer
Dual-LLM / Models
Physics Engine
Monte Carlo Core
Data Layer
Room / SQLite
External APIs
6 Free Services
End-to-End Data Flow (14 Steps)
1–2. User inputs vehicle → Auto-geocode via Nominatim
3–4. Weather fetch (Open-Meteo) → Elevation fetch (3-point gradient)
5–6. Route fetch (OSRM) → Overpass road context (200m bbox)
7. Physics Engine: N=50 Monte Carlo iterations; stochastic perturbations
8. ML Fusion: Φ_driving, terrain multiplier, AC factor, traffic idle
9. Statistics: mean CO₂, 5th/95th percentile bounds, mean fuel/energy
10. AI Insights: rule-based on-device evidence engine
11. Route Ranking: OSRM alternatives → physics+ML per route
12. Segment Analysis: per-leg terrain, road type, speed limit
13. Visualisation: BarChart (CO₂ breakdown) + PieChart (energy share)
14. Persistence: Room DB → TripEntity with all metrics
Output: Mean CO₂ + 90% CI, fuel/energy estimates, AI recommendations, route comparison, PDF report generation
Key Design Choice: All core APIs are free/open-source — zero variable cost for deployment at scale.
Chapter 3 — System Design
9 / 21

## Slide 10
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Three-Layer Computational Model
Layer 1: Physics Engine
Deterministic vehicle dynamics based on Newton's 2nd law:
Ftotal = Froll + Faero + Fgrade + Facc
• Rolling resistance: m × g × Crr
• Aerodynamic drag: 0.5 × ρ × Af × Cd × v²
• Grade resistance: m × g × sin(θ)
• Inertial force: m × a
Monte Carlo: N=50 stochastic iterations over speed, headwind, gradient
Layer 2: ML Telemetry Fusion
Four telemetry-derived adjustments:
• Φdriving — behaviour coefficient from acceleration & jerk
• kterrain — gradient multiplier (1.00–1.12)
• FAC — AC thermal penalty (0.85 when on)
• CO₂idle — traffic congestion idle emissions
CO₂final = (CO₂base × Φ × k) / FAC + CO₂idle
Layer 3: AI Recommendations
Tier 1 — On-Device LLM:
MediaPipe GenAI (Gemma 3/4, Phi-2, Falcon 7B)
Offline, zero data tx, sub-second latency
Tier 2 — Cloud Fallback:
Gemini 1.5 Flash / Claude 3 Sonnet
AES-encrypted API keys
Tier 3 — AutonomousAgent:
Weekly personalised telemetry reports
Key Use Cases (12 Primary)
UC-01 Select Vehicle (100+ Indian models) | UC-02 Auto-Fetch Telemetry (5 APIs) | UC-03 Estimate CO₂ (Physics + ML) | UC-04 Live GPS Tracking
UC-05 Compare Eco Routes (OSRM) | UC-06 Analyse Route Segments | UC-07 Sensitivity Study (2,000 MC iterations) | UC-08 AI Chat (8 models)
UC-09 Weekly AI Agent Report | UC-10 Dashboard / History (Room DB) | UC-11 Download On-Device LLM | UC-12 Export PDF Report
All core functionality uses exclusively free, open-source APIs — zero variable cost for deployment.
Chapter 3 — System Design
10 / 21

## Slide 11
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Technology Stack & APIs
Category | Technology / Library | Purpose / Notes
Language / SDK | Java 8 + Android SDK | API Level 24–34 (Android 7.0+), Gradle 8.13
UI Framework | Material Design 3 | AppCompat, ConstraintLayout, CoordinatorLayout
Mapping / Routing | osmdroid 6.1.18 + OSRM | OpenStreetMap tiles; polyline overlays; free routing API
Weather / Elevation | Open-Meteo + Open Elevation | WMO weather codes, temp, wind, humidity; 3-point terrain gradient
Road Context | Overpass API (OSM) | 200m bounding-box query: highway type, landuse, traffic signals
Charts | MPAndroidChart v3.1.0 | Bar + Pie charts for emissions and energy breakdown
On-Device AI | MediaPipe GenAI 0.10.20 | Gemma 3/4, Phi-2, Falcon 7B — INT4 quantised .task/.bin
Cloud AI (opt.) | Google Gemini / Anthropic Claude | gemini-1.5-flash; claude-3-sonnet; AES-encrypted API keys
Database | Room 2.6.1 (SQLite) | TripEntity, TripDao — async queries; history by Today/Week/Month/All
Security | AES Encryption | SecurityManager: all API keys encrypted in SharedPreferences
Chapter 3 — System Design
11 / 21

## Slide 12
04
IMPLEMENTATION
Physics Engine, ML Fusion Layer, Dual-LLM Architecture & UI

## Slide 13
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Physics Engine & ML Fusion
Force Model & Energy Computation
Ftotal = Froll + Faero + Fgrade + Facc
Emech = Ftotal × v × t (Joules)
Fuel energy = Emech / ηeng
Powertrain-specific CO₂ computation:
• Petrol: 32 MJ/L → 2.31 kg CO₂/L
• Diesel: 36 MJ/L → 2.68 kg CO₂/L
• CNG: 47.7 MJ/kg → 2.75 kg CO₂/kg
• EV: 0.716 kg CO₂/kWh (Indian grid)
ML Telemetry Adjustments
Driving Behaviour Coefficient:
λaccel = 0.05 + min(Δv/10.0, 0.10)
Φdriving = 1.0 + (λaccel × Δv) + λjerk
AC Thermal Penalty: FAC = 0.85 (when AC on)
Terrain Multipliers (kterrain):
Plains 1.00 | Arterial 1.01 | Urban 1.03
Rolling Hills 1.06 | Hilly/Mountain 1.12
Final: CO₂final = (CO₂base × Φ × k) / FAC + CO₂idle
Monte Carlo Simulation: N = 50 iterations per estimation, with stochastic perturbations over speed fluctuation, headwind, and road gradient variance. Results sorted to produce mean CO₂, 5th-percentile lower bound, and 95th-percentile upper bound — yielding a statistically valid 90% confidence interval that distinguishes EcoDrive from simplistic point-estimate calculators.
Chapter 4 — Implementation
13 / 21

## Slide 14
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Dual-LLM Architecture & Application UI
Tier 1: On-Device LLM
• MediaPipe GenAI 0.10.20
• Gemma 3 1B/4B, Gemma 4 E2B/E4B
• Phi-2, Falcon 7B
• Offline, zero data transmission
• Sub-second response latency
• 528 MB model size (INT4)
Tier 2: Cloud Fallback
• Google Gemini 1.5 Flash
• Anthropic Claude 3 Sonnet
• User-configurable preference
• AES-encrypted API key storage
• Triggered on low-confidence
• High-capability responses
Tier 3: AutonomousAgent
• Weekly personalised reports
• Comprehensive telemetry analysis
• Structured [CONFIDENCE: N] score
• Driving pattern insights
• Actionable recommendations
• Powered by DualLLMRouter
Route & CO₂ Calculator
Route CO₂ Comparator
Sensitivity Analysis
System Settings
Chapter 4 — Implementation
14 / 21

## Slide 15
05
RESULTS & VALIDATION
Experimental Validation, Emission Estimates & Sensitivity Analysis

## Slide 16
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Emission Estimation Results
Vehicle / Fuel | Scenario | Mean CO₂ | Mean Fuel | 90% CI | g/km
Maruti Swift (Petrol 1.2L) | 12 km Urban, High traffic, AC On | 1.82 kg | 0.61 L | [1.65, 2.01] | 151.7
Maruti Swift (Petrol 1.2L) | 12 km Urban, Low traffic, AC Off | 1.31 kg | 0.45 L | [1.19, 1.44] | 109.2
Mahindra XUV700 (Diesel 2.2L) | 25 km Highway, AC On | 3.12 kg | 1.16 L | [2.90, 3.35] | 124.8
Tata Nexon EV | 20 km Urban, AC On | 2.87 kg* | N/A | [2.51, 3.24] | 143.5
Honda City CNG (1.5L) | 15 km Rolling terrain | 2.21 kg | 0.80 kg | [2.05, 2.38] | 147.3
Generic Petrol SUV | 10 km Hilly, Aggressive driving | 2.48 kg | 1.07 L | [2.18, 2.78] | 248.0
* EV CO₂ represents grid electricity carbon (0.716 kg/kWh Indian grid), not tailpipe emissions
Chart: g/km
| Swift Urban AC | Swift Low Tr. | XUV700 Hwy | Nexon EV | City CNG | SUV Hilly
CO₂ (g/km) | 151.7 | 109.2 | 124.8 | 143.5 | 147.3 | 248
Validation Summary:
Tested on iQOO 13 (Snapdragon 8 Elite, 16 GB RAM, Android 15)
• Estimates consistent with CPCB and ARAI BS-VI benchmarks
• Offline functionality verified (physics + on-device AI)
• 4G LTE network tests for OSRM and Open-Meteo confirmed
• 90% CI provides honest uncertainty representation
Chapter 5 — Results & Validation
16 / 21

## Slide 17
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Monte Carlo Sensitivity Analysis
Parameter | Range Tested | Key Finding | Sensitivity
Speed | 10–120 km/h | U-shaped; min at 60–70 km/h; drag ∝ v² above 80 | High
Acceleration | 0.0–4.0 m/s² | >2 m/s² increases CO₂ by 15–25% | High
Traffic | 0.0–1.0 ratio | Fully congested adds ~40–60% idle emissions | High
AC Activation | On / Off | ~15–18% CO₂ increase; larger at low speeds | Medium
Terrain | Plains → Hilly | Hilly adds 12% over plains baseline | Medium
Air Density | 0.9–1.3 kg/m³ | ±5% variation; significant at high speeds | Low–Med
Variance Contribution Breakdown
Chart: 
| Traffic congestion | Driving behaviour | Speed selection | AC usage | Terrain/grade
pct | 30 | 25 | 20 | 15 | 10
Key Insight: Traffic congestion (~30%) and driving behaviour (~25%) together account for over half of emission variance — making them the highest-impact targets for eco-driving interventions. Speed selection (~20%) shows the U-shaped efficiency curve with optimal band at 60–70 km/h.
Chapter 5 — Results & Validation
17 / 21

## Slide 18
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Application Dashboard & AI Insights
EcoDrive Core — Trip Estimation
Weekly AI Telemetry Report
All-Time Emissions Dashboard
Eco-Assistant AI Chat
Dashboard Features:
• Total CO₂ Footprint — trip-level and all-time aggregation with emission breakdown pie chart (core physics vs. context penalty)
• Emissions Over Time — bar chart tracking trends across Today / Week / Month / All tabs
• Autonomous AI Insight — weekly personalised telemetry report with driving pattern analysis, terrain context, and 5 actionable recommendations
• Eco-Assistant Chat — natural language Q&A for eco-driving advice, route optimisation, and personalised insights (on-device + cloud fallback)
• Live GPS Tracking — real-time speed, route polyline on OpenStreetMap, background foreground service
• System Settings — cloud AI key management, on-device model download (Gemma/Phi-2/Falcon), place learning toggle, PDF/CSV export
Chapter 5 — Results & Validation
18 / 21

## Slide 19
06
CONCLUSION & FUTURE WORK
Summary of Contributions, Limitations, and Development Roadmap

## Slide 20
INTRODUCTION SYSTEM ANALYSIS SYSTEM DESIGN IMPLEMENTATION RESULTS CONCLUSION
Limitations & Future Scope
Current Limitations
1. No OBD-II Integration — static vehicle database vs. real-time engine load, RPM, throttle position data
2. Fixed Grid Factor — Indian electricity grid carbon intensity fixed at 0.716 kg CO₂/kWh; no state/time-of-day variation
3. Limited Behaviour Quantification — driving coefficient from speed differential only; no smartphone IMU accelerometer data
4. On-Device LLM Capability — MediaPipe Gemma provides basic Q&A but lacks parametric knowledge of full cloud models
Future Development Roadmap
1. OBD-II Bluetooth Fusion — RFCOMM protocol for real-time engine parameters; accuracy ±15% → ±5%
2. Fleet Management Module — multi-user backend (Firebase/PostgreSQL) for aggregating driver emission profiles
3. Federated Learning — personalise driving/terrain multipliers from historical trip data, preserving privacy
4. VAHAN / FASTag Integration — automatic vehicle parameter lookup by registration number
5. Carbon Credit Gamification — convert kg CO₂ saved into equivalent carbon credits
Conclusion: EcoDrive successfully demonstrates a physics-grounded, AI-augmented mobile application for real-time vehicular CO₂ emission estimation. The system integrates deterministic vehicle dynamics, Monte Carlo probabilistic simulation, real-time GPS/weather telemetry, and a dual-tier LLM architecture — all within a single Android application targeting the Indian automotive context.
Chapter 6 — Conclusion & Future Work
20 / 21

## Slide 21
THANK YOU
Questions & Discussion
Key Contributions of This Project:
1. Multi-fuel physics engine (Petrol, Diesel, CNG, EV) under unified force-energy-emission framework
2. ML telemetry fusion with Monte Carlo 90% confidence intervals
3. Dual-LLM architecture: on-device MediaPipe GenAI + cloud Gemini/Claude fallback
4. Complete Android app: GPS tracking, route comparison, trip history, PDF reports
References
[1] CPCB, "Air Quality Index – Annual Report," 2023. [2] ARAI, "Emission Factors for Indian Vehicles – BS-VI," TR-2022-47, 2022.
[3] SIAM, "Indian Automobile Industry Data," 2024. [4] EEA, "COPERT v5.6," 2023. [5] Google, "MediaPipe LLM Inference API," 2024.
[6] OSRM, "Open Source Routing Machine v5.x," 2024. [7] OpenWeatherMap, "Current Weather API v2.5," 2024.
[8] Android Developers, "Room Persistence Library," 2024. [9] MPAndroidChart v3.1.0. [10] CEA, "CO₂ Baseline Database v18," 2023.